## Slide 1: Transfer optimizations on partitioned communication
Axel Schneewind

## Slide 2: MPI-4.1: Nonblocking Communication Operations
Progress. A call to MPI_WAIT that completes a receive will eventually terminate and return if a matching send has been started , unless the send is satisfied by another receive.
In particular, if the matching send is nonblocking, then the receive should complete even if
no call is executed by the sender to complete the send. Similarly, a call to MPI_WAIT that
completes a send will eventually return if a matching receive has been started, unless the
receive is satisfied by another send, and even if no call is executed to complete the receive.

## Slide 3: MPI-4.1: Nonblocking Communication Operations
Order. Nonblocking communication operations are ordered according to the execution
order of the calls that initiate the communication.
The nonovertaking requirement of Section 3.5 is extended to nonblocking communication, with this definition of order being
used.

## Slide 4: MPI-4.1: Partitioned Communication
Rationale. Partitioned communication is designed to provide opportunities for MPI implementations to optimize data transfers. MPI is free to choose how many transfers to do within a partitioned communication send independent of how many partitions are reported as ready to MPI through MPI_PREADY calls.
Aggregation of partitions is permitted but not required.
Ordering of partitions is permitted but not required.
A naive implementation can simply wait for the entire message buffer to be marked ready before any transfer(s) occur and could wait until the completion function is called on a request before transferring data.
However, this modality of communication gives MPI implementations far more flexibility in data movement than nonpartitioned
communications. (End of rationale.)

## Slide 5
Progress
  No software progress threads
  Offloading to hardware
Partitions are mapped to a partitioned send request, started by Pready()
  No guarantee that transfer occurs on Pready()
State of implementations - OpenMPI

## Slide 6
A single transfer is initiated after all Pready()-calls have been made
  No overlap
State of implementations - MPICH

## Slide 7
Goals
Measure effective bandwidth depending on message size
Do different MPI-implementations perform optimizations (aggregation, reordering) on partitioned transfers?
Is it possible to trigger early progress using completion tests?
Do OpenMPIs Point-to-point Messaging Layer (PML) – components make use of hardware offloading?

## Slide 8
Benchmarking scheme
// initialization
for i in 0...num_iterations:
MPI_Barrier(); // synchronization
s_i = MPI_Wtime();
MPI_Start(&request);
for p in 0...partition_count in some order:
perform some MPI operation to send/receive partition p
MPI_Wait(&request, &status);
e_i = MPI_Wtime();
// cleanup

## Slide 9
Benchmarks
Mode | initialization | ready | completion | 
 |  | MPI_Send |  | 
 | MPI_Send_init | MPI_Start | MPI_Waitall | 
 |  | MPI_Isend | MPI_Waitall | 
 | MPI_Psend_init | MPI_Pready | MPI_Wait | 
 | MPI_Psend_init | MPI_Pready | MPI_Wait | MPI_request_get_status
 | MPI_Win_create | MPI_lock MPI_Put MPI_unlock |  | 
 | MPI_Win_create | MPI_lock Mpi_Put MPI_unlock |  | 

## Slide 10
OpenMPI: Send->Recv

## Slide 11
OpenMPI: ISend->IRecv

## Slide 12
OpenMPI: Pready

## Slide 13
OpenMPI: MPI_Win per partition

## Slide 14
OpenMPI: MPI_Win for entire buffer

## Slide 15
Results: Psend on MPICH-4.1.2

## Slide 16: Program Day 2:

## Slide 17: IPTW 2023
International Parallel Tools Workshop, 5./6. October 2023
Thanks for participating!